## Slide 1: Basics of Mobile Robotics. Final Project
Elisa Ferrara
Cédric Fournier
Simon Gmür
Edgar Aellen
19/12/2023

## Slide 2: Computer vision
ArUco Library
Detect Marker Candidates
Analyse Marker Codification
Color detection
Define the color of the obstacles
Selection the pixels of the same color in the image

## Slide 3: Global Path Planning
Alogrithm A*
Problem :
  Too much point
  Robot going slow
  Risk of missing a point
Solution :
  Keypoints
  Reduce the number of point
  Strategic point -> angle
  Increase the robot speed
  Keep the precision
Recurring problem :
  Computation time

## Slide 4: Local Obstacles Avoidance
Potential field
Problem : obstacle on keypoint
Solution : ignoring keypoint if angle between robot direction and keypoint higher than an angle threshold

## Slide 5: Kalman Filtering
Estimating position including information from camera and odomtry
MODEL
  State: (x,y, θ)
  Inputs: right_speed, left_speed  Extended Kalman Filter for non linear systems
PROCESS NOISE
  Gaussian White Noise of covariance Q due to slippering and errors in motor speed sensors
MEASUREMENT NOISE
  Gaussian White Noise of covariance R due to errors in the camera measurements and Computer Vision algorithm

## Slide 6: Control: Path Following
P controller
Basic P controller
If angle between robot direction and orientation goal too high :
  Robot stop and turn
Else : P controller classic
Local avoidance :
  Sum of the global speed and local speed to avoid the obstacle